## Slide 1: Assurance Case
TianyuanWu 63305667

## Slide 2
G2: To prove the consistency across UPPAAL model, Simulink model and hardware implementation.
S1: Use model-based Analysis to prove functionality and safety of pacemaker.
G1: DDD Pacemaker is safe to patient under any heart condition and meet all functionality requirements.
C1: A DDD pacemaker is a medical cyber physical system which can sense both atrial and ventricular events and give pace to both atrial and ventricular
G3: To prove UPPAAL model meets all safety requirements.
C2:Heart condition: Cardiac electrophysiology which can be detected by a pacemaker.
J1: Use timed automaton based software model can correctly simulate heart and pacemaker.
C3: A timed automaton is a finite automaton extended with a finite set of real valued clocks. .
S2: Use validation to check the Simulink model satisfies functional requirements and cover all possible states.
S3: Use risk management to manage all possible risks and mitigate all possible hazards

## Slide 3
G2: To prove the consistency across UPPAAL model, Simulink model and hardware implementation.
J2: The correctness of Simulink coder is proved. So the Simulink model and hardware implementation are in consistence.
S4: Use traceability analysis to prove the consistence between UPPAAL model and Simulink model.
G4: To prove Simulink model is identical with UPPAAL model
E1: All parameters, variables, states and transitions between UPPAAL model and Simulink model is fully mapped.
E2: Giving same input to two models, same output can be observed.
C4: If these 3 models are proved identical, prove the safety and functionality of any one model can indicate the safety and functionality of hardware.
G5: Use conformance test to prove Simulink model covers all possible heart states.
E3: A 100% covered test case was generated, and it can pass conformance test under this full covered testcase.

## Slide 4
G3: To prove UPPAAL model meets all safety requirements.
C5: Because of the proof of G2, safety of UPPAAL model implies the safety of hardware pacemaker.
S3: Use TCTL queries to prove it meets safety requirements.
G6: Prove UPPAAL model does not contain deadlocks.
G7: Prove UPPAAL model can always maintain intervals between heart beats no longer than lower rate interval (LRI).
G8: Prove UPPAAL model can always maintain intervals between heart beats no shorter than upper rate interval (URI).
C6: A deadlock-free model indicates it will never got stuck.
E4: property
A[] (not deadlock) satisfied
E5: property
A[] (PLRL.two_v imply PLRL.t<=TLRI)
satisfied
E6: property
A[] (PURL.interval imply PURL.t>=TURI)
satisfied
J3: If all following queries are satisfied, then it will always maintain patients' heart rate in a normal interval (i.e. safety to patients).

## Slide 5
G9: To validate Simulink model is functional
J3: If the pacemaker model can pass all functional test and conformance test, it can be proved to have required function.
E7: It works as expect under (Ain, Vin), (Ain, VP), (AP, Vin) and (AP, VP). All functional test passed.
S2: Use validation to check the Simulink model satisfies functional requirements.
C7: Validation and functional test can prove that the pacemaker is in indented use.
C8: Test functions can generate same inputs with heart model, and is able to simulate all heart conditions.

## Slide 6
S3: Use risk management to manage all possible risks and mitigate all possible hazards
G11: Prove pacemaker syndrome hazards are mitigated.
C9: A pacemaker should always not make heart condition worse, so all possible risks caused by pacemaker should be considered, and fatal cases are not allowed.
J4:ATR and ELT situations are not fatal to patients, consider less of these cases are acceptable.
E9: According to the risk management report, PVARP and AVI considered. A and V events will never be too close to each other.
E10: According to the risk management report, VRP and LRI in considered, so this pacemaker will never paces on T wave.
G10: Prove bradycardia (slow atrial rate and slow ventricular rate) hazards are mitigated.
E8: According to the risk management report, LRI and URI considered, so heart rate is always maintained in safe interval .
G12: Prove Pace on T wave hazards are mitigated.